## Slide 1
Nov. 6th 2017
The 35th IEEE ICCD@Boston, USA
Shinpei Kato
Graduate School of
Information Science and
Technology
The University of Tokyo
Takuya Azumi
Graduate School of
Engineering Science
Osaka University
Yuya Maruyama
Graduate School of
Engineering Science
Osaka University
Exploring Scalable Data Allocation
and Parallel Computing on NoC-based Embedded Many Cores
Notes: Today, I am going to talk about our work titled “Exploring Scalable Data Allocation and Parallel Computing on NoC-based Embedded Many Cores”.

## Slide 2: Necessity and Importance of Embedded Many Cores
In embedded systems, high processing demand and low power consumption are needed.
Ex. self-driving system
[Introduction]
Application
Runtime
OS
Hardware
ROS
Recognition
Many
cores
RTOS
Decision
Actuate
GPU
FPGAs
Radar
Camera
GNSS
OpenCV
CUDA
PCL
Real-time Linux
ECUs
Control
LiDAR
AUTOSAR
self-driving system
CAN
Ether
Notes: In recent years, embedded systems have become increasingly complicated and diverse.
Self-driving vehicles are one of this complicated and diverse systems.
In many domains, high processing demand and low power consumption are needed.

## Slide 3: Necessity/Importance of Embedded Many Cores
[Introduction]
Applicatino
Runtime
OS
ROS
認知
RTOS
判断
操作
OpenCV
CUDA
PCL
Real-time Linux
制御
AUTOSAR
self-driving system
Embedded
Real-time
High performance
We need heterogeneous systems.
In embedded systems, high processing demand and low power consumption are needed.
Ex. self-driving system
Hardware
Many
cores
GPU
FPGAs
Radar
Camera
GNSS
ECUs
LiDAR
CAN
Ether
Notes: To meet this demands, we need heterogeneous systems such as coexistence of many cores, GPU, and FPGA.
Combining the advantages of each platform, we think that heterogeneous computing can meet embedded and real-time requirements and realize high performance with reasonable power consumption.
In our work, we focus on the many-core computing platforms.

## Slide 4: Comparison of many core architecture
 | Non-Cluster | Cluster
NoC Architecture |  | 
Programmability | ✓ | 
Scalability |  | ✓
[Introduction]
memory
core
core
memory
core
core
core
core
core
core
core
core
core
core
core
core
core
core
core
core
core
core
core
core
memory
core
core
core
core
memory
core
core
core
core
memory
core
core
Network-on-Chip (NoC)
Notes: Subsequently, we compare two types of many-core Network-on-Chip architecture.
One is Non-Cluster architectures, and the other is Cluster Architecture.
In the former, all cores share large memories with large bandwidth.
In contrast, in Cluster architectures, several cores gather to form a cluster and distributed memories are connected to the network on chip.
In our work, we explore latter cluster architectures for scalability.

## Slide 5: KALRAY MPPA-256
[System Model]
NoC-based Embedded Many Cores: MPPA-256
  Scalability: 256 + 16 cores
  High power efficiency: 16/24W
  NoC (Network-on-Chip)
  non-uniform memory access (NUMA)
16 x 16 = 256
16 computing cores per cluster
shared memory (SRAM 2MB) per cluster
NoC interface
Compute Cluster
4 IO cores per cluster
shared memory (SRAM 2MB + DDR 2GB)
NoC interface
Ethernet, PCIe
I/O Cluster
Notes: We adopt KALRAY MPPA as Network-on-chip-based embedded many core platform.
This has more than 256 cores on NoC and high power efficiency for embedded computing.
A cluster of 16 cores called Compute Cluster shared 2 MB SRAM memory.
These memories of 16 clusters are connected to NoC.
For I/O, a cluster of 4 cores called IO Cluster contains 2 MB SRAM and 2 GB DDR memories.

## Slide 6: KALRAY MPPA-256
[System Model]
NoC-based Embedded Many Cores: MPPA-256
  Scalability: 256 + 16 cores
  High power efficiency: 16/24W
  NoC (Network-on-Chip)
  non-uniform memory access (NUMA)
16 computing cores per cluster
shared memory (SRAM 2MB) per cluster
NoC interface
Compute Cluster
4 IO cores per cluster
shared memory (SRAM 2MB + DDR 2GB)
NoC interface
Ethernet, PCIe
I/O Cluster
Notes: Actual network on chip is like this.
Distributed memories on NoC realize high scalability of the number of cores.

## Slide 7: Two evaluations on NoC-based Embedded Many Cores
[Practical Application]
The scalability of parallelization in many-core processors based on NoC is observed in a real complex application as a part of a self-driving driving system.
[Contribution]
[NoC Data Transfer]
The evaluations of the data transfer on DMA-capable NoC quantitatively characterize the end-to-end latencies, which depend on the routing, DMA configurations, and memory type.
Notes: This is a brief summary of our work.
We provide two contributions on NoC-based embedded many-core platform.
One is the evaluation of NoC data transfer between memories.
The other is parallelization of practiceal application on MPPA.
In this talk, we focus on the latter part.

## Slide 8: Two evaluations on NoC-based Embedded Many Cores
[Practical Application]
The scalability of parallelization in many-core processors based on NoC is observed in a real complex application as a part of a self-driving driving system.
[Contribution]
[NoC Data Transfer]
The evaluations of the data transfer on DMA-capable NoC quantitatively characterize the end-to-end latencies, which depend on the routing, DMA configurations, and memory type.
Self-driving application on Real-time OS on Embedded Many Cores
Evaluation
Parallelization
Test course
Simulation
Notes: We port and parallelize a part of self-driving application on real-time Operating System on embedded many cores.

## Slide 9: Self-driving/Localization
[Practical Application]
3D map data
3D laser scan
NDT matching
Current position
Estimate current position by matching 3D map data and 3D laser scan
NDT Matching Algorithm
- PCL (open source Point Cloud Library)
- LIDAR (Laser Imaging Detection and Ranging)
- SLAM (Simultaneous Localization And Mapping)
- NDT (Normal Distributions Transform)
Notes: We parallelize localization algorithm of self-driving application because it is important and requires high processing demand in self-driving systems.
This algorithm estimates a current position on the map by matching the 3D map data and 3D laser scan.

## Slide 10: Self-driving/Localization/Parallelization
Parallelize part of the bottleneck
[Practical Application]
Chart: 
| radiusSearch | derivatives | others
4 | 4.439 | 4.993 | 1.24
Chart: execution time [s]
| Normal | Parallelized
computeTransform | 0.298 | 0.078
Others | 0.006 | 0.004
Deadline
100 ms
TODO
Notes: Here is a pie chart showing the bottleneck part of the algorithm.
As you can see in this chart, two parts occupy almost 90%.
Light blue part corresponds to a nearest neighbor search.
Blue part corresponds to a computation of evaluation function by derivatives for convergence of newton method.
We parallelize the latter part and accelerate execution time from 300 ms to 80 ms in the right graph.
In many self-driving systems, laser sensors get data with 10 Hz, so that deadline can be assumed with 100 ms.

## Slide 11: Self-driving/Localization/Parallelization/Video
[Practical Application]
powered by
Notes: This is demonstration video in our test course.
We plug MPPA and lap top computer to network in the car.
Steering, accelerator, and brake are automatically controlled based on the result of MPPA.
(Algorithms except for localization runs on the lap top computer and we use Autoware, which is open-source software for urban autonomous driving. Upper left values are MPPA processing time with seconds and car speed with km/h.)

## Slide 12: Summary and Future Work
[Practical Application]
Confirm the scalability of parallelization in a real complex application
[Conclusion]
[Future Work]
Parallelize remains of self-driving localization and other algorithms
Run benchmark applications such as Rodinia for furthermore analysis
[NoC Data Transfer]
Analyze end-to-end latencies, which depend on the routing, DMA configurations, and memory type
Notes: In our work, we provide two contributions as shown in the slide.
This is a very early stage of the self-driving application on the embedded many-core platform.
In future work, we have to parallelize remains of self-driving localization and other algorithms. In addition, we would like to run benchmark applications such as Rodinia for furthermore analysis.

## Slide 13: Software Stack
[Practical Application]
Application
Runtime
OS
Localization algorithm of self-driving application
CC1
CC2
IO
CC16
Cluster
Memory
SMEM
SMEM
ROS
Real-Time OS (eMCOS)
…
Network
NoC
Ether
MPPA
SMEM
SMEM
DDR
PCL
LibNoC
…
Notes: This is software stack for self-driving application on many cores.
Based on MPPA, we adopt eMCOS which is a real-time operating system provided by a Japanese supplier, eSOL.
It is hard to run existing other operating systems because cores of MPPA does not guarantee cache coherency and require high parallelism.
We build application on several runtime middleware and libraries.
ROS means Robot Operating System which is not OS but runtime library and tool for robot operating.
PCL means Point Cloud library which handles point cloud scanned by laser sensor on a car.
I will explain brief algorithm of localization algorithm of self-driving application and PCL in the next slide.

## Slide 14: KALRAY MPPA-256
[System Model]
NoC-based Embedded Many Cores: MPPA-256
  Scalability: 256 + 16 cores
  High power efficiency: 16/24W
  NoC (Network-on-Chip)
  non-uniform memory access (NUMA)
16 x 16 = 256
16 computing cores per cluster
shared memory (SRAM 2MB) per cluster
NoC interface
Compute Cluster
4 IO cores per cluster
shared memory (SRAM 2MB + DDR 2GB)
NoC interface
Ethernet, PCIe
I/O Cluster
Notes: We adopt KALRAY MPPA as Network-on-chip-based embedded many core platform.
This has more than 256 cores on NoC and high power efficiency for embedded computing.
A cluster of 16 cores called Compute Cluster shared 2 MB SRAM memory.
These memories of 16 clusters are connected to NoC.
For I/O, a cluster of 4 cores called IO Cluster contains 2 MB SRAM and 2 GB DDR memories.

## Slide 15: KALRAY MPPA-256
[System Model]
NoC-based Embedded Many Cores: MPPA-256
  Scalability: 256 + 16 cores
  High power efficiency: 16/24W
  NoC (Network-on-Chip)
  non-uniform memory access (NUMA)
DDR
16 computing cores per cluster
shared memory (SRAM 2MB) per cluster
NoC interface
Compute Cluster
4 IO cores per cluster
shared memory (SRAM 2MB + DDR 2GB)
NoC interface
Ethernet, PCIe
I/O Cluster
DDR
Ether
Ether
Notes: For I/O, a cluster of 4 cores called IO Cluster contains 2 MB SRAM and 2 GB DDR memories.
They also connected to NoC.

## Slide 16: KALRAY MPPA-256
[System Model]
NoC-based Embedded Many Cores: MPPA-256
  Scalability: 256 + 16 cores
  High power efficiency: 16/24W
  NoC (Network-on-Chip)
  non-uniform memory access (NUMA)
16 computing cores per cluster
shared memory (SRAM 2MB) per cluster
NoC interface
Compute Cluster
4 IO cores per cluster
shared memory (SRAM 2MB + DDR 2GB)
NoC interface
Ethernet, PCIe
I/O Cluster
Notes: Actual network on chip is like this.
Distributed memories on NoC realize high scalability of the number of cores.

## Slide 17: KALRAY MPPA-256
[System Model]
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
4
4
4
4
Core layer
Memory layer
Network layer
Core
Memory
Network
NoC-based Embedded Many Cores: MPPA-256
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M + 2G
2M + 2G
2M
2M
Notes: We adopt KALRAY MPPA as Network-on-chip-based embedded many core platform.
This has more than 256 cores on NoC and high power efficiency for embedded computing.
A cluster of 16 cores called Compute Cluster shared 2 MB SRAM memory.
These memories of 16 clusters are connected to NoC.
For I/O, a cluster of 4 cores called IO Cluster contains 2 MB SRAM and 2 GB DDR memories.

## Slide 18: Comparison of many core architecture
 | Non-Clusters | Clusters
Architecture |  | 
Reusability | ○ | △
Scalability | △ | ○
Power Efficiency | △ | ○
[Introduction]
memory
memory
Network-on-Chip (NoC)
…
…
…
…
core
core
…
core
core
…
…
…
…
core
core
core
core
memory
…
core
core
core
core
Bus
Notes: So far, I have talked about necessity and importance of embedded many-core platforms.
Secondly, we compare two type of many-core architecture.
One is Uniform Memory Access, and the other is Non-Unified Memory Access.
In Uniform Memory Access, all cores share one large memory with large bus.
All cores are connected equally to the memory.
This is the same architecture of single/multi core platform, so that existing software
So that
In contrast, in Non-Uniform Memory Access, core memory

## Slide 19
R0
R1
R128
R129
R2
R3
R130
R131
R8
R9
R4
R5
R10
R11
R6
R7
R192
R193
R12
R13
R194
R195
R14
R15
R160
R162
R161
R163
R224
R226
R225
R227

## Slide 20: KALRAY MPPA-256
[System Model]
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
4
4
4
4
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M
2M + 2G
2M + 2G
2M + 2G
2M
Notes: We adopt KALRAY MPPA as Network-on-chip-based embedded many core platform.
This has more than 256 cores on NoC and high power efficiency for embedded computing.
A cluster of 16 cores called Compute Cluster shared 2 MB SRAM memory.
These memories of 16 clusters are connected to NoC.
For I/O, a cluster of 4 cores called IO Cluster contains 2 MB SRAM and 2 GB DDR memories.