## Slide 1
Yue Hou Azumi Takuya
Saitama Univ. Saitama Univ.
Japan Japan
Energy Consumption Prediction Framework in Model-based Development for Edge Devices
May. 13th 2024
RAGE
Notes: Hello, everyone. My name is Yue Hou, a graduate school student from Saitama University in Japan.
Today, I’ll give a presentation on my research which names [Energy Consumption Prediction Framework in Model-based Development for Edge Devices}

## Slide 2: Outline
Background
Proposed Method
Evaluation
Conclusion

## Slide 3: Edge Devices
[Background]
Development of Edge Devices
  The count of devices is increasing
  Systems is becoming complex
Development of Systems on Edge Devices
  The cost is becoming significant
  The reusability of the code developed with traditional method is limited

## Slide 4: Model-based Development (MBD)
[Background]
MATLAB/Simulink
  MATLAB: a programming and numeric computing platform developed by MathWorks
  Simulink: a block diagram environment for Model-based Development integrated with MATLAB

## Slide 5: Model-based Development (MBD)
[Background]
V-Model
  A structured approach to system development that mirrors the stages of development with corresponding testing phases
Required Specifications
Basic Design
Detailed Design
Code Generation
System Test
Integration Test
Unit Test
Notes: The V-Model in Model-Based Development
The V-Model is a structured approach to system development that mirrors the stages of development with corresponding testing phases, forming a V-like diagram. It is especially prevalent in Model-Based Development (MBD), where the emphasis is on developing and validating system models early in the design process.

## Slide 6: Model-based Development (MBD)
[Background]
Design Phase
  Requirements Analysis
  Basic Design: simulation based on model (Energy is ignored)
  Detailed Design
Required Specifications
Basic Design
Detailed Design
Code Generation
System Test
Integration Test
Unit Test
Design Phase
Test Phase
Notes: The V-Model in Model-Based Development
The V-Model is a structured approach to system development that mirrors the stages of development with corresponding testing phases, forming a V-like diagram. It is especially prevalent in Model-Based Development (MBD), where the emphasis is on developing and validating system models early in the design process.

## Slide 7: Low Level Virtual Machine Intermediate Representation （LLVM-IR）
[Background]
LLVM-IR
  A low-level programming language used as the primary IR within the LLVM compiler framework
  Serves as a bridge between high-level languages and the machine code, enabling code analysis and transformation
Notes: The V-Model in Model-Based Development
The V-Model is a structured approach to system development that mirrors the stages of development with corresponding testing phases, forming a V-like diagram. It is especially prevalent in Model-Based Development (MBD), where the emphasis is on developing and validating system models early in the design process.

## Slide 8: Contribution
[Proposed Method]
［Contribution1］ A schema is proposed to describe the energy consumption of instructions
［Contribution2］ A method is proposed for extracting the working portion from generated code and transforming it into LLVM-IR
［Contribution3］ A software tool is designed to predict model energy consumption

## Slide 9: Contribution
[Proposed Method]
［Contribution1］ A schema is proposed to describe the energy consumption of instructions
［Contribution2］ A method is proposed for extracting the working portion from generated code and transforming it into LLVM-IR
［Contribution3］ A software tool is designed to predict model energy consumption

## Slide 10: Energy Consumption Description Schema
Schema
  Provide a universal framework to describe energy consumption for any given instruction
[Proposed Method]

## Slide 11: Energy Consumption Description Schema
Three-Tier Structure
  Top Layer
    CommonInstructionSet
  Middle Layer
    Instruction
  Bottom Layer
    PowerConsumption
[Proposed Method]

## Slide 12: Energy Consumption Description Schema
Acquisition Method
  Time and Energy
    Execution time is directly linked to energy consumption
  Method
    A cyclic execution approach is used for better precision in predicting individual instructions' time and energy use
[Proposed Method]
Empty Body
Measured Body

## Slide 13: Contribution
[Proposed Method]
［Contribution1］ A schema is proposed to describe the energy consumption of instructions
［Contribution2］ A method is proposed for extracting the working portion from generated code and transforming it into LLVM-IR
［Contribution3］ A software tool is designed to predict model energy consumption

## Slide 14: Extracting Working Portion
Function Call
  Call the main function section in the generated file by means of a function call in the new c-file
[Proposed Method]

## Slide 15: Contribution
[Proposed Method]
［Contribution1］ A schema is proposed to describe the energy consumption of instructions
［Contribution2］ A method is proposed for extracting the working portion from generated code and transforming it into LLVM-IR
［Contribution3］ A software tool is designed to predict model energy consumption

## Slide 16: Prediction Tool
Input
  Schema
  LLVM-IR Code
Output
  Prediction of code’s energy consumption
[Proposed Method]

## Slide 17: Comparison with Other Methods
 | Modeling | Code Generation | Energy Consumption Measurement | Energy Consumption Prediction
MDD [7] | ○ | ○ |  | 
Mercury [8] | ○ | ○ |  | 
IEEE Access [9] |  |  | ○ | 
SDK4ED [10] |  |  | ○ | ○
J4CS [11] |  |  | ○ | ○
PARTSim [12] |  |  | ○ | ○
本研究 | ○ | ○ | ○ | ○
必要なら関連研究との差異や新規性の説明
[Proposed Method]

## Slide 18: Experimental Environment
[Evaluation]
Target device
  SONY Spresense (ARM Cortex M4F)
Measurement device
  AVHzY CT-3 USB tester

## Slide 19: Experimental
Basic Evaluation
  Measure the power consumption and execution time of basic instructions on the target device
  Create test scripts to obtain actual execution time and power consumption in a single core environment
[Evaluation]
Notes: Code execution time is closely related to energy consumption, and to predict energy consumption, code time estimation can be synchronized and used as a validation.
To this end, we have listed the following basic evaluations
To guarantee cross-platform and cross-architecture properties, the Low Level Virtual Machine Intermediate Representation (LLVM-IR) code is used in the experiment.
LLVM-IR provides a unified, hardware-independent basic instruction set.
First, it measures the power consumption and execution time of the basic instructions on the target device.
We also create a test script to obtain the actual execution time and power consumption in a single-core environment.
Finally, based on the measured single instruction data, predictions are made at the LLVM-IR instruction level and compared to the measured values to analyze the prediction accuracy.
The figure shows the measured power consumption and execution time of a number of basic instructions. The unit of execution time is cycles, and the unit of energy is nanojoules

## Slide 20: Experimental
Basic Evaluation
  Test Scripts
    Four arithmetic operations（add,sub,mul,div）
  Predicting power consumption
    Focus on the “for” statement part
[Evaluation]
Test Scripts
Power Consumption Prediction Focus on “for”
Time and Energy Consumption of Instructions
Notes: In order to verify the feasibility of our proposed approach
The test script performs a simple four arithmetic operations.
in this case, we focus only on the for statement, so when the number of loops is small, the error is large.As the number of loops is increased, the error gradually decreases.

## Slide 21: Experimental
Evaluation with Models
[Evaluation]
Overall Model Construction
For Iterator Subsystem Construction
Notes: In addition, an evaluation using a model was conducted to determine if the proposed schema and estimation method are applicable in model-based development.
The model we prepared is shown in the figure below, using the for subsystem to perform the four arithmetic operations.
In the actual case, the model works by receiving information from the outside and passing it to the model after the process is complete, and the test model is also used in the function call.

## Slide 22: Experimental Environment
Evaluation with Models
  Code generated by Embedded Coder
  Execute in user code with function calls
  Convert to LLVM-IR instructions
  Make predictions with a prediction tool
[Evaluation]
Notes: Once the model has been created, Embedded Coder generates the code.
The for statement part of the generated code is shown in the figure on the left
.Next, it writes in the user's code with a function call
Finally, the actual power consumption is calculated by writing to the target device.

## Slide 23: Experimental Environment
Evaluation with Models
  Result
    Prediction
      2,059,200,000 nJ
    Measurement
      1,980,000,000 nJ
    Error: 4%
  Error Analysis
    Precision of the equipment
      1,000 times per second
[Evaluation]
Notes: The prediction part converts the user code into LLVM-IR instructions, and the prediction is performed by the designed prediction tool.
The resulting error between actual and predicted power consumption is found to be 4%.

## Slide 24: ＜サブタイトル＞
[今後の展望]
今後の展望については，最終発表では隠しスライドにする

## Slide 25: Conclusion
Background
  Development of edge devices is becoming complex
  The reusability of the code developed with traditional method is limited
  Energy consumption of system is ignored in MBD
Proposed Method
  Schema Construction: a structured approach to modeling energy usage
  Module Extraction: parts of the model relevant to energy consumption
  Energy Consumption Prediction Tool: software to predict energy usage
Contribution
  provides a robust method for estimating energy requirements in embedded systems
Evaluaion
  Basic evaluation with test scripts
  Evaluation with models
Notes: まとめは以下のようになっています。
発表は以上です。

## Slide 26: ＜サブタイトル＞
[補足資料]

## Slide 27: 新規性は何ですか?

## Slide 28: 何が難しいんですか?

## Slide 29: 実装で何が難しかったですか?

## Slide 30: 既存研究と比べて何が良いんですか？

## Slide 31: 既存研究で提案手法が使われないのは何故?

## Slide 32: どこまでが自分で提案した部分ですか

## Slide 33: 何故この研究をやろうと決めたのですか？

## Slide 34: この研究に必要性はあるのか？

## Slide 35: 想定しているユーザは誰ですか？

## Slide 36: 工夫したことは何ですか？

## Slide 37: その評価を選んだ理由は何ですか？

## Slide 38: 評価は優位的な差があると言えるのか?

## Slide 39: 今後の展望などはありますか？